## Slide 2: Relationship
LSS (Philion et al.)
BEVDet (Huang et al.)
BEVFormer (Li et al.)

## Slide 3
ECCV 2022
세미나 발표자 : 김형균 (PseudoLab 10th)

## Slide 4: Relationship
LSS (Philion et al.)
2020-08
BEVDet (Huang et al.)
2022-06
BEVFormer (Li et al.)
2022-07
Simple-BEV (Adam et al.)
2022-09
PETRv2 (Liu et al.)
2022-11
BEVDepth (Yinhao et al.)
2022-11
FB-BEV (Zhiqi et al.)
2023-08
PointBeV (Loick et al.)
2024-05
BEVFusion (Zhijian et al.)
2024-09
GaussianBeV (Florian et al.)
2024-12
2021
2022
2023
2024
2025
Bottom-Up (2D → 3D)
Top-Down (3D → 2D)
Ref. Ma, Yuexin, et al. "Vision-centric bev perception: A survey." IEEE Transactions on Pattern Analysis and Machine Intelligence (2024).
Colored : Camera-only
Bold : Attention mechanism

## Slide 5: Agenda
Problem Definition
Methodology: BEVFormer
Experiment Results
Key takeaways

## Slide 6: Problem Definition

## Slide 7: Problem Definition
Multi-Camera 기반 3D Perception: Bird’s-Eye View (BEV) Representation
  Lidar 센서에 비해 저렴한 가격
  원거리 및 고해상도 정보 습득 가능
  주행에 필요한 Vision-based 이미지 감지 가능 (e.g., 주행 신호, 정지선, 횡단보도 등)
Camera-view 이미지를 통한 Object detection 과 Segmentation task
Figure : Caesar, Holger, et al. "nuscenes: A multimodal dataset for autonomous driving." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2020.

## Slide 8: Problem Definition
기존의 Multi-Camera BEV Representation Models
Depth Information 기반
  e.g., Lift-Splat-Shoot, BEVDet, …
  Bottom-Up Method (2D → 3D)
  Depth Estimation에서 누적된 오차가 Downstream Task 성능 저하에 큰 영향
Temporal Information 사용 X
  Temporal Information의 활용 가능성
    움직이는 물체 추적
    가려진 물체 추론
    물체의 속도 추론

## Slide 9: Problem Definition
Depth Information 기반
  e.g., Lift-Splat-Shoot, BEVDet, and so on
  Bottom-Up Method (2D → 3D)
  Depth Estimation에서 누적된 오차가 Downstream Task 성능 저하에 큰 영향
Temporal Information 사용 X
  Temporal Information의 활용 가능성
    움직이는 물체 추적
    가려진 물체 추론
    물체의 속도 추론
BEVFormer: Multi-Camera BEV Representation via Spatiotemporal Transformer
Spatial
Cross-Attention

## Slide 10: Problem Definition
Depth Information 기반
  e.g., Lift-Splat-Shoot, BEVDet, and so on
  Bottom-Up Method (2D → 3D)
  Depth Estimation에서 누적된 오차가 Downstream Task 성능 저하에 큰 영향
Temporal Information 사용 X
  Temporal Information의 활용 가능성
    움직이는 물체 추적
    가려진 물체 추론
    물체의 속도 추론
BEVFormer: Multi-Camera BEV Representation via Spatiotemporal Transformer
Spatial
Cross-Attention
Temporal
Self-Attention

## Slide 11: Problem Definition
Depth Information 기반
  e.g., Lift-Splat-Shoot, BEVDet, and so on
  Bottom-Up Method (2D → 3D)
  Depth Estimation에서 누적된 오차가 Downstream Task 성능 저하에 큰 영향
Temporal Information 사용 X
  Temporal Information의 활용 가능성
    움직이는 물체 추적
    가려진 물체 추론
    물체의 속도 추론
BEVFormer: Multi-Camera BEV Representation via Spatiotemporal Transformer
Spatial
Cross-Attention
Temporal
Self-Attention
Grid-shaped BEV Queries

## Slide 12: Methodology
BEVFormer: Multi-Camera BEV Representation via Spatiotemporal Transformer

## Slide 13: Methodology - BEVFormer
Overview

## Slide 14: Methodology - BEVFormer
Overview
Spatial
Cross-Attention
Temporal
Self-Attention
Grid-shaped
BEV queries

## Slide 15: Methodology - BEVFormer
Overview
Spatial
Cross-Attention
Temporal
Self-Attention
Grid-shaped
BEV queries

## Slide 16: Methodology - BEVFormer
Overview
Spatial
Cross-Attention
Temporal
Self-Attention
Grid-shaped
BEV queries

## Slide 17: Methodology - BEVFormer
Grid-shaped BEV Queries
  BEV Queries() 와 BEV Features()의 크기는 서로 동일
  각 Grid point P=( x, y )에서의 Query feature :
  각 Grid point와 Ego Vehicle 간의 실제 거리 e.g., W = 200, H = 200, s = 0.512m, Grid 좌표 (100,100) → 실제 (0m, 0m) Grid 좌표 (90,120) → 실제 (-5.12m, 10.24m)
Ego
(100,100)
(200, 200)
(0, 0)
0
255
BEV Queries / Features

## Slide 18: Methodology - BEVFormer
Temporal Self-Attention (TSA)
  RNN 과 Self-Attention 메커니즘 컨셉을 적용
  RNN 이전 타임스탬프의 BEV Feature ()의 정보를 현재 타임스탬프의 BEV Queries ()에 반영
  Self-Attention BEV Query ()에서 각각의 위치 마다, 관련이 높을 것으로 예상되는 주변 위치의 BEV Feature () 정보를 에 반영
NOTE! Training과 Inference의 효율을 높이기 위해, Deformable DETR(Zhu et al., 2020) [1] 의 Attention 메커니즘을 활용.
BEVFormer
(TSA + …)
[1] Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).

## Slide 19: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Ego Vehicle의 움직임 정보를 바탕으로 t-1의 BEV Feature 들의 위치 조정*
Notes: Nuscenes 데이터의 각 Scene마다 ego vehicle 의 infos[‘ego2global_translation’], infos[‘ego2global_rotation’]를 사용하여, Bt-1의 Alignment를 진행.
코드 상에서는 can_bus 라는 Key에 이 정보를 저장하여 사용. -> 실제 차량의 CAN 통신 정보와 Matching 하기 위함으로 보임.

## Slide 20: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
?
Ego Vehicle의 움직임 정보를 바탕으로 Feature 들의 위치 조정*
Notes: Nuscenes 데이터의 각 Scene마다 ego vehicle 의 infos[‘ego2global_translation’], infos[‘ego2global_rotation’]를 사용하여, Bt-1의 Alignment를 진행.
코드 상에서는 can_bus 라는 Key에 이 정보를 저장하여 사용. -> 실제 차량의 CAN 통신 정보와 Matching 하기 위함으로 보임.

## Slide 21: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Ego Vehicle의 움직임 정보를 바탕으로 Feature 들의 위치 조정*
Query feature at p :
Input Feature Map :

## Slide 22: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Ego Vehicle의 움직임 정보를 바탕으로 Feature 들의 위치 조정*
Query feature at p :
Input Feature Map :
논문에선 사용
Notes: 논문에서는 8개의 head와 4개의 reference point를 사용 -> 총 32개의 Sampled attention key를사용.

## Slide 23: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Ego Vehicle의 움직임 정보를 바탕으로 Feature 들의 위치 조정*
Query feature at p :
Input Feature Map :
논문에선 사용

## Slide 24: Methodology - BEVFormer
Temporal Self-Attention (TSA) ← Deformable Attention
Query feature at p :
Input Feature Map :
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Ego Vehicle의 움직임 정보를 바탕으로 Feature 들의 위치 조정*
논문에선 사용

## Slide 25: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
Temporal Self-Attention 이 적용된
BEV Query

## Slide 26: Methodology - BEVFormer
Temporal Self-Attention 이 적용된
BEV Query
Spatial Cross-Attention (SCA)
1. Hit Views 선정
2. BEV Query와 Multi-Camera Feature 간의 Cross-Attention (Multi-Scale Deformable Attention)

## Slide 27: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
  Hit Views 선정 BEV Query 의 각 Point 에 대응되는 Camera Image 의 Feature 만을 사용하기 위함
    Grid 내 Point 의 실제 거리
    높이 정보를 고려하기 위해 를 추가
    Camera의 Extrinsic & Intrinsic 정보를 바탕으로 계산된 Projection Matrix 를 사용하여 각 Camera의 2D 이미지에 투영
cam 1
cam 2
cam 3
cam 4
cam 5
cam 6
BEV Query
Notes: Nref = 4 (-5m to 3m, but in the code, 0.5m to 7.5m, Double-check)
Projection matrix of cameras ← Nuscenes cams..‘sensor2lidar_translation’ and ‘sensor2lidar_rotation’

## Slide 28: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
  BEV Query와 Multi-Camera Feature 간의 Cross-Attention
Query feature at p :
Input Feature Map :
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Notes: 8 heads, 8 points, 4 level

## Slide 29: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
  BEV Query와 Multi-Camera Feature 간의 Cross-Attention
cam 1
cam 4
Backbone Multi-Scale Features e.g., FPN[1]
[1] Lin, Tsung-Yi, et al. "Feature pyramid networks for object detection." Proceedings of the IEEE conference on computer vision and pattern recognition. 2017.
of at
1/64
1/32
1/16
l=1
l=2
l=3
1/64
1/32
1/16
l=1
l=2
l=3
Notes: 8 heads, 8 points, 4 level

## Slide 30: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
  BEV Query와 Multi-Camera Feature 간의 Cross-Attention
Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Notes: 8 heads, 8 points, 4 level

## Slide 31: Methodology - BEVFormer
Spatial Cross-Attention (SCA)
  Hit Views 선정
  BEV Query와 Multi-Camera Feature 간의 Cross-Attention
Query feature at p :
Input Feature Map :
Figure : Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
Notes: 8 heads, 8 points, 4 level

## Slide 32: Methodology - BEVFormer
Recap

## Slide 33: Experiments

## Slide 34: Experiment Setup
Training
  Dataset
    NuScenes Dataset [1] : 3D OD + Seg
    Waymo Open Dataset [2] : 3D OD
  Backbone
    ResNet101-DCN (FCOS3D [3])
    VoVnet-99 (DD3D [4])
  Head
    3D OD : Deformable DETR [5]
    Panoptic SegFormer [6]
  Loss Function
    3D Object Detection Task : L1 loss
    Segmentation Task : Generalized IoU loss
[1] Caesar, Holger, et al. "nuscenes: A multimodal dataset for autonomous driving." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2020.
[2] Sun, Pei, et al. "Scalability in perception for autonomous driving: Waymo open dataset." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2020.
[3] Wang, Tai, et al. "Fcos3d: Fully convolutional one-stage monocular 3d object detection." Proceedings of the IEEE/CVF international conference on computer vision. 2021.
[4] Park, Dennis, et al. "Is pseudo-lidar needed for monocular 3d object detection?." Proceedings of the IEEE/CVF International Conference on Computer Vision. 2021.
[5] Zhu, Xizhou, et al. "Deformable detr: Deformable transformers for end-to-end object detection." arXiv preprint arXiv:2010.04159 (2020).
[6] Li, Zhiqi, et al. "Panoptic segformer: Delving deeper into panoptic segmentation with transformers." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2022.
BEVFormer
3D Object Detection
Segmentation
BEVFeature
BEVFeature

## Slide 35: Experiment Results
Camera-only Baseline 모델 (Attention X)에 비해, 9.0 Points 높은 NDS 퍼포먼스와 현저히 줄어든 Velocity 예측 에러를 보여줌.
Lidar 센서를 사용한 Baseline 모델에 준하는 NDS 퍼포먼스를 보여줌.
Notes: nuScenes detection score (NDS): We consolidate the above metrics by computing a weighted sum: mAP, mATE, mASE, mAOE, mAVE and mAAE.
mean Average Precision (mAP): We use the well-known Average Precision metric, but define a match by considering the 2D center distance on the ground plane rather than intersection over union based affinities.
Average Translation Error (ATE): Euclidean center distance in 2D in meters.
Average Scale Error (ASE): Calculated as 1 - IOU after aligning centers and orientation.
Average Orientation Error (AOE): Smallest yaw angle difference between prediction and ground-truth in radians. Orientation error is evaluated at 360 degree for all classes except barriers where it is only evaluated at 180 degrees. Orientation errors for cones are ignored.
Average Velocity Error (AVE): Absolute velocity error in m/s. Velocity error for barriers and cones are ignored.
Average Attribute Error (AAE): Calculated as 1 - acc, where acc is the attribute classification accuracy. Attribute error for barriers and cones are ignored.

## Slide 36: Experiment Results
2D → 3D 기반 Baseline 모델인 VPN과 LSS 보다 전반적으로 향상된 퍼포먼스를 보여줌.
BEVFormer 모델의 Multi-Task Learning 적용 가능성을 확인. (예외, Road and Lane Segmentation)
* BEVFormer-S Spatial Cross-Attention만 적용된 BEVFormer

## Slide 37: Experiment Results
BEVFormer는 Object Visibility 가 낮은 (0-40 %) 환경에서도 Robust한 퍼포먼스를 보여줌.
특히, Visibility가 낮은 환경에서, Temporal information이 3D Object의 Translation, Orientation, 그리고 Velocity 예측 에러를 줄이는 데 효과적임을 보여줌.

## Slide 38: Key takeaways

## Slide 39: Key takeaways
BEVFormer
  BEV map의 각 위치에서의 Feature 정보를 Spatiotemporal Attention Mechanism을 활용하여 Multi-camera image로부터 효율적으로 추출
  Depth Estimation의 오차로부터 자유로운 Top-Down (3D → 2D) 방식의 방법론.
  Camera만 사용하더라도 Lidar 사용 모델과 대등한 수준의 퍼포먼스.

## Slide 40: Thanks !